## Slide 1: Verification Framework
Test bench development and its validation
UCSD WES Cohort 9, All Rights Reserved.

## Slide 2: LTE Test Signal
Generate the LTE Downlink RMC waveform from LTE Waveform Generator in Matlab and export the waveform to Matlab and convert it IQ waveforms
RF coverage from 325 MHz to 3.8 GHz, with up to 20 MHz of instantaneous bandwidth
One transmitter and one receiver, half or full duplex
Reference Links:
https://github.com/analogdevicesinc/TransceiverToolbox/tree/pluto_lte_app/trx_examples/streaming/LTE_PA_App
https://plutosdr.org/lte-enb-transmitter-conformance-tests-using-adalm-pluto/
https://www.mathworks.com/help/supportpkg/plutoradio/ref/plutoreceiver.html
UCSD WES Cohort 9, All Rights Reserved.

## Slide 3: Test Bench Demo
  LTE Cell scanner open-source software from GitHub
  First verified with NAR bands – 900MHz, able to detect different MIB’s from different Cells
  Picked non-NAR region band – 860MHz to generate LTE Test signal
  Generated LTE Test signal using Matlab– 5MHz, 25 RB, 64QAM, Cell ID: 11 with PSS, SSS, PBCH.
  Exported this signal to MatLab to play from Pluto SDR
  Play LTE test signal continuously from Pluto SDR and run cell search algorithm in PYNQ to capture the transmitted LTE test signal
RTL
Digitizer
UCSD WES Cohort 9, All Rights Reserved.

## Slide 4: Spectrum Analyzer
RFSoC 2x2 overlays
  The base overlay is included in the PYNQ image for the RFSoC 2x2 board
  The base design includes a bitstream with IP which allows to use the RF ADCs and DACs on the board
  Up to 2 GHz bandwidth for inspection
  Inspect range 0 - 4.096 GHz
  Adaptive bandwidth control and center frequency selection
  Reprogrammable windowing
  Hardware accelerated processing (time domain → frequency domain → power spectrum [dB])
  PYNQ abstracted allowing Python to interface with the hardware
  Plotly visualization of spectrum and spectrogram (waterfall)
  Simple dashboard for more convenient control/visualization
Reference Links:
https://www.rfsoc-pynq.io/overlays.html
https://www.rfsoc-pynq.io/base_overlay.html
git clone https://github.com/Xilinx/RFSoC2x2-PYNQ.git
https://github.com/strath-sdr/rfsoc_sam
https://github.com/strath-sdr/rfsoc_ofdm
UCSD WES Cohort 9, All Rights Reserved.